## Slide 1
Development of Software for Parameter Estimation and its Application on Wind Power Plant Equivalent Model
São Carlos School of Engineering - EESC
University of São Paulo - USP
Gabriel José Negrelli Gomes
Advisor: Prof. Dr. Elmer Pablo Tito Cari

## Slide 2: Introduction
Increase in renewables participation
Mainly solar and wind energy
Clean alternative to fossil fuels
Rely on weather condition

## Slide 3: Introduction
Worldwide increase leaded by:
United States
China
European Union
  2010 bill
  Reduce greenhouse emissions by 20% (1990 levels)
  20% share of renewables by 2020

## Slide 4: Introduction
Brazilian Panorama:
2002 bill
Creates PROINFA
Increase wind, solar, small hydro and biomass share
Renewables supplying 10% of energy by 2024

## Slide 5: Wind Energy
Wind energy benefited from these policies
European Union:
  417 TWh in 2019
  15% of electricity demand (1% higher than 2018)
  192 GW of installed capacity (UK included)

## Slide 6: Wind Energy
Source: WindEurope, 2020

## Slide 7: Wind Energy
Brazil
  48.5 TWh in 2018 (Itaipu: 96.5 TWh)
  8.1% of electricity demand (14.4% higher than 2017)
  15.5 GW of installed capacity

## Slide 8: Wind Energy
Source: ABEEolica, 2020

## Slide 9: Wind Energy
Brazil
  Energy yield yet to be explored
  Potential to generate 272 TWh
  144 TWh in the Northeast Region
  Complimentary regimes of wind and water (São Francisco River)

## Slide 10: Wind Energy
Source: ANEEL, 2005

## Slide 11: Wind Energy
Growth expectations for this source
Disadvantages:
  Stochastic source
  Not evenly distributed
  Generators with low inertia
    Affects system stability

## Slide 12: Wind Energy
Study of effects of these plants on stability
Need of mathematical models
Multiple generators
Equivalent model
Source: Adapted from (MULJADI; ELLIS, 2008)

## Slide 13: Research Goals
Development of software for parameter estimation
  Package with estimation framework
  Graphical user interface (GUI)
Application on wind power plant equivalent model

## Slide 14: Wind Turbine Generators

## Slide 15: Wind Turbine Generators
Huge variety of generators
Task force to develop generic models
Four types of wind turbine generators
Representation of wind power plants by one machine

## Slide 16: Wind Turbine Generators
Type-1 Wind Turbine (SCIG):
Squirrel-Cage Induction Generator
Operates at constant speed
Reactive compensation

## Slide 17: Wind Turbine Generators
Type-1 Wind Turbine (SCIG):

## Slide 18: Wind Turbine Generators
Type-2 Wind Turbine (WRIG):
Wound Rotor Induction Generator
Rotor resistance variation
Reactive compensation

## Slide 19: Wind Turbine Generators
Type-2 Wind Turbine (WRIG):

## Slide 20: Wind Turbine Generators
Type-2 Wind Turbine (WRIG):
Alter torque-speed curve
Operates within a small speed range

## Slide 21: Wind Turbine Generators
Type-3 Wind Turbine (DFIG):
Doubly Fed Induction Generator
Wound Rotor Induction Generator + frequency converter
Operates at ± 30% of rated speed
Reactive injection control

## Slide 22: Wind Turbine Generators
Type-3 Wind Turbine (DFIG):

## Slide 23: Wind Turbine Generators
Type-4 Wind Turbine:
Induction/Synchronous Generator
Grid connection through converter
Wide speed range
Reactive injection control

## Slide 24: Wind Turbine Generators
Type-4 Wind Turbine:

## Slide 25: Wind Turbine Generators
Source: JRC, 2017

## Slide 26: Wind Power Plant Model

## Slide 27: Wind Power Plant Model
Represent Type-3 and 4 Generators
Behaviour of wind power plants
Transient studies

## Slide 28: Wind Power Plant Model
Source: Adapted from (ERLICH et al., 2012)

## Slide 29: Wind Power Plant Model
If :
and
Else if :
and
Else if :
and

## Slide 30: Wind Power Plant Model
PI block:
Phase shift:

## Slide 31: Wind Power Plant Model
Delay blocks:
Outputs:

## Slide 32: Wind Power Plant Model

## Slide 33: Wind Power Plant Model
Represent Type-3 and -4 Generators
Behaviour of wind power plants
Transient studies
Disadvantages:
  PMUs required to obtain angle measurement

## Slide 34: Proposed Wind Power Plant Model
Source: Adapted from (ERLICH et al., 2012)

## Slide 35: Proposed Wind Power Plant Model

## Slide 36: Parameter Estimation Method

## Slide 37: Parameter Estimation Method

## Slide 38: Parameter Estimation Method
Hybrid Approach
Metaheuristic – Mean-Variance Mapping Optimization (MVMO)
  Fast error reduction at the beginning
  Slow convergence
Nonlinear method – Trajectory Sensitivity Method (TSM)
  Fast convergence
  Initial point dependence

## Slide 39: MVMO
Population-based metaheuristic
Offspring considering population statistics
Great results for small populations

## Slide 40: MVMO
Setup
Population size
Number of offspring
Number of genes for mutation
Selection method
Normalized search region

## Slide 41: MVMO
Best
Worst

## Slide 42: MVMO
Mutation
Mapping function
  Based on mean and variance

## Slide 43: MVMO
Mean and variance effects

## Slide 44: MVMO
Asymmetrical shape factors

## Slide 45: TSM
Based on Newton-Raphson
Fast convergence
Initial values dependence

## Slide 46: TSM
Expanding Taylor’s Series:
At the iteration:

## Slide 47: TSM
Derivatives are obtained by approximation
where

## Slide 48: Hybrid Method Application
Spring-Mass System
Real parameters

## Slide 49: Hybrid Method Application
Spring-Mass System
TSM
  1st Case:
  2nd Case

## Slide 50: Hybrid Method Application
Spring-Mass System
MVMO
  20 individuals

## Slide 51: Hybrid Method Application
Spring-Mass System
Hybrid Approach
  20 individuals

## Slide 52: Hybrid Method Application
Approach | Time | Final Error |  | 
TSM | 7 s |  | 3.08 | 6.15
MVMO | 10 s |  | 3.45 | 5.96
Hybrid | 12 s |  | 3.08 | 6.15
Approach | Time | Final Error |  | 
TSM | 7 s |  | 3.08 | 6.15
MVMO | 10 s |  | 3.45 | 5.96
Hybrid | 12 s |  | 3.08 | 6.15

## Slide 53: Software Developed

## Slide 54: Software
identPy:
  Framework for parameter estimation
identPy_GUI:
  Graphical User Interface for framework
Python
Non-specific

## Slide 55: Software

## Slide 56: Results

## Slide 57: Results
Synthetic data from simulated system
Fault in grid bus in

## Slide 58: Results
MVMO settings
15 individuals
5000 generations

## Slide 59: Results
TSM settings
Starting point from MVMO
7 iterations

## Slide 60: Results
Estimation in 8 seconds
Final error of

## Slide 61: Results

## Slide 62: Results
Effects of population size on MVMO
5 population sizes evaluated
35 estimations for each population

## Slide 63: Results
Estimation of Proposed WPP Model
Simulation using estimated parameters

## Slide 64: Results
Estimation of Proposed WPP Model
Estimation using MVMO
  15 individuals
  5000 generations

## Slide 65: Results
Estimation of Proposed WPP Model
Process took 19 minutes

## Slide 66: Results

## Slide 67: Conclusion

## Slide 68: Conclusion
Framework and Software available at GitHub
  Users can download, test and contribute with project
Application of software into WPP model problem
  Estimation using a hybrid approach (MVMO + TSM)
Proposal of WPP model
  Avoid necessity of PMUs in the grid

## Slide 69: Ongoing Research

## Slide 70: Ongoing Research
Proposed WPP model
  Assessment on model behavior
Hybrid Method
  Implementation of other estimation methods

## Slide 71
Thank you!

## Slide 72
Development of Software for Parameter Estimation and its Application on Wind Power Plant Equivalent Model
São Carlos School of Engineering - EESC
University of São Paulo - USP
Gabriel José Negrelli Gomes
Advisor: Prof. Dr. Elmer Pablo Tito Cari

## Slide 73: Hybrid Estimation – Load Model
Linearized Z-IM Load Model
Impedance
Third-Order Induction Motor

## Slide 74: Hybrid Estimation – Load Model
Linearized Z-IM Load Model

## Slide 75: Hybrid Estimation – Load Model
Linearized Z-IM Load Model

## Slide 76: Hybrid Estimation – Load Model
Linearized Z-IM Load Model
  5 individuals

## Slide 77: MVMO Process

## Slide 78: MVMO Process